## Slide 1: Solving the Current Replacement Value (CRV) Riddle

## Slide 2: Introductions

## Slide 3: Introductions
Bill Roth
  President & CEO of Roth IAMS
  Co-Founder of SLAM Technologies
  Nearly 30 years of experience collaborating with public sector institutions across North America on all aspects of facility and infrastructure asset management
  Active member of several industry associations such as APPA (National, Regional and Local), NSPMA, NASFA, etc.

## Slide 4: Introductions
30 Years of Expertise – Extensive experience in architecture, construction, training, and data analytics across public and private sectors.
Facility Management Leader – Led CAD standards, accessibility studies, CMMS selection, and facility condition assessments at TVDSB.
Strategic Capital Planner – Helps clients prioritize deferred maintenance and develop long-term capital plans.
SLAM Champion – Manages Customer Success Coordinators and drives platform improvements based on user needs.
Ayden Townsend Practice Leader, Data Management, Roth IAMS

## Slide 5: AGENDA
Introductions
Why CRV Matters
Four Common Methods to Calculate CRV
Special Considerations
Q & A
Picking What’s Right For You

## Slide 6: Setting the Table Why CRV Matters

## Slide 7: Why CRV Matters
Without CRV you cannot calculate your Facility Condition Index (FCI)
FCI = Sum of Deferred Capital Renewal Needs for a Defined Period of Time x100
Current Replacement Value
FCI is the industry standard for benchmarking your buildings across your portfolio
Foundational piece of integrated asset management
Millions of dollars are spent getting the Deferred Capital Renewal Need, yet CRV is often an afterthought
Many organizations have struggled to get numbers they can trust

## Slide 8: Why CRV Matters
“Internal” consistency is more important than accuracy
  If your CRV is too high, your FCI values will be artificially low
  If your CRV is too low, your FCI values will be artificially high
A stable CRV (one that doesn’t change too much over time) provides more reliable data for decision-making

## Slide 9: It’s time for A Poll question

## Slide 10: Four common methods for calculating crv

## Slide 11: Insurable Value
When securing insurance on a building, your insurance company will ask for an Insurable Value, which is used as the basis of a “total loss” in the underwriting
Generally calculated using an industry-standard cost guide based on the construction of the building (e.g. Marshall & Swift)
  Can be very detailed and building-specific
If your organization already has them and is using them in other areas of your operations, they can be easy and “free” to secure

## Slide 12: Insurable Value
CHALLENGES
  How were the numbers originally calculated?
    Many of these values are legacy values where the people who developed them are no longer around
    Was the same methodology used for buildings over time
  How have they been increased/inflated over the years?
  Have they been updated based on upgrades or additions to the building?
  May not be available for all asset types
    e.g. Surface and subsurface infrastructure

## Slide 13: Insurable Value
WHEN TO USE IT
  When you have the numbers
  When you know how they were calculated originally
  When you know that the numbers have been updated

## Slide 14: Simple Square Footage
Develop a single or categorical cost/sq.ft. for each building type
Apply it based on the size of the building
Easy to consistently apply across the portfolio
Simple and easy to explain to non-facilities stakeholders

## Slide 15: Simple Square Footage
Simple Square Footage Example |  |  | 
Building Type | Unit Cost ($/sq.ft.) | Building Size (sq.ft.) | CRV
Elementary School A | $250 | 50,000 | $12,500,000
Elementary School B | $250 | 65,000 | $16,250,000
Secondary School C | $400 | 150,000 | $60,000,000
Administrative Building | $550 | 75,000 | $41,250,000

## Slide 16: Simple Square Footage
CHALLENGES
  Simplicity starts to fall away if you have too many different types of buildings
  Need to have accurate building sizes
  Less accurate if you have diverse design and construction standards across similar asset types
    If buildings were calculated over the course of decades, standards and codes, and likely even elements present will vary
  Need to have confidence in the unit costs and how they were developed
    Can’t just pull them out of the air or “spit ball” them

## Slide 17: Simple Square Footage
WHEN TO USE IT
  A few unique types of buildings within your portfolio
  Similar design and construction standards
  Buildings located within a smaller geographic area
  Municipalities, school districts, housing

## Slide 18: Sum of the Parts
CRV = Sum of All Element Replacement Values (ERVs)
  Like building your car from parts
Based on the real-world elements within each building
Integrated within many Capital Asset Management Systems
  It’s just math!
Relatively easy to explain to non-facility stakeholders

## Slide 19: Sum of the Parts
CHALLENGES
  Requires a Facility Condition Assessment (FCA) to get ERVs
  Dependant upon the quality and depth of your FCA
    Were all elements captured, or just those that need attention within the short term
    Was anything missed?
    Can fluctuate greatly when you do a new FCA (if things that were missed or were out-of-scope previously are picked up)
      Causes big swings in FCI before and after a new FCA

## Slide 20: Sum of the Parts
WHEN TO USE IT
  High level of trust in your FCAs and your element costs
  Senior executives understand that there may be variation over time in your FCI

## Slide 21: Weighted square footage
A modified version of the Simple Square Footage method used for buildings with multiple space uses
  Develop unit costs for different types of space usage/program that are applied based on the area of each space

## Slide 22: Weighted square footage
Weighted Cost CRV Calculation Example |  |  | 
Space Type | Unit Cost | Square Footage | Space Cost
Classroom | $400 | 100,000 | $40,000,000
Laboratory | $750 | 175,000 | $131,250,000
Office | $550 | 25,000 | 13,750,000
CRV |  |  | $185,000,000
Blended Cost/sq.ft. |  |  | $616.67

## Slide 23: Weighted square footage
CHALLENGES
  Requires an accurate space inventory
  More complex and harder to explain to non-facilities stakeholders
  Need to have accurate unit costs for each space type
  Keeping area for each space type updated

## Slide 24: Weighted square footage
WHEN TO USE IT
  Complex portfolios with many multi-use facilities
  Where you have or can get up-to-date, accurate space measurements

## Slide 25: It’s time for A Poll question

## Slide 26: Special considerations

## Slide 27: Special Consideration
Regional Factors
  If you have a geographically diverse portfolio need to account for regional cost differences
Soft Costs
  CRV only includes labor and materials, so you need to account for things like Project Management, Design, Contingency, etc.
Difficulty Factor
  Unique circumstances that can impact costs such as heritage buildings, specialized finishes, etc.

## Slide 28: Special Consideration
EXTRA SPECIAL CASE
  Buildings on a campus that are connected to a Central Utility Building
    Have lower HVAC costs compared to stand-alone buildings
  Central Plants themselves are very complex and hard to template
    Better to just develop a building-specific cost based on the actual equipment within the building

## Slide 29: Picking what is right for you

## Slide 30: What Way is Right for Me?
Portfolio Characteristics – Uniform vs. diverse assets.
Data Availability – Do you have up-to-date IVs or asset inventories?
Accuracy vs. Simplicity – Is ease of use more important than precision?
Consistency Over Time – Can you maintain the same methodology?

## Slide 31: In Summary
CRV is an important part of your Asset Management Planning
Consistency is More Important than Accuracy
Pick the Right Method for You and Your Portfolio
DON’T SAY DEFERRED MAINTENANCE!!!!

## Slide 32: One more thing

## Slide 34: Q & A

## Slide 35
For More Thought Leadership
Scan the QR Code!

## Slide 36
THANK YOU FOR ATTENDING
Connect with us directly
  bill.roth@rothiams.com
  US - (727) 247-9419
  CA – (416)-700-6678
  ayden.townsend@rothiams.com
Visit our website at rothiams.com
Follow us on LinkedIn