## Slide 1: ACCESSIBILITY COMPLIANCE BEYOND MINIMUM CODE

## Slide 2: introduction
Andrew Chow, P.Eng., M.Eng., CPI, RHFAC Professional Practice Leader - Accessibility, Senior Facility Assessor, Technical Reviewer, Roth IAMS
14 years of building condition assessment experience
11 years accessibility audit experience
Responsible for creating methodology and approach for accessibility audits at Roth IAMS
Rick Hansen Foundation Accessibility Certified
One of the primary assessors for IFAs

## Slide 3
Agenda
Limitations of Current Standards
Emerging Trends & Best Practices
Overcoming Real-World Constraints
Auditing Beyond Compliance
Accessibility Needs & Universal Design
Future-Proof Strategy
Q&A

## Slide 4: KEY QUESTIONs
Are your facilities truly accessible, or just barely compliant?
How do I exceed minimum code requirements?

## Slide 5: KEY QUESTION
Before aiming to exceed code, we should understand :
  What do we need to address?
  What is the end result we want to achieve?

## Slide 6: Overview of Disabilities
Image source: Pulrang, Andrew (2019). What Defines Members Of The “Disability Community?”
https://disabilitythinking.com/disabilitythinking/2019/9/15/cukmbl2x4k5eyvo2jj63lq9unifpwi

## Slide 7: Overview of Disabilities
Oftentimes, we limit accessibility to wheelchair access only
We emphasize creating space for mobility
Image source: International Symbol of Access (ISA) and Modified ISA
https://en.wikipedia.org/wiki/International_Symbol_of_Access

## Slide 8: Various Disabilities
We must understand that there are a variety of disabilities that need to be addressed.
Image source: https://greatcareers.org/neurodiversity-in-the-workplace-and-international-day-of-persons-with-disabilities/
Other disabilities to consider:
  Vision
  Hearing
  Pain-related
  Neurological

## Slide 9: Means of Accessibility
Other than addressing paths of travel, we will have to address other disability needs in our facilities or built environment.

## Slide 10: Universal Design vs. Barrier-free

## Slide 11: Disability Types & Demographics
Who We Are Designing For
Statistics Canada, Canadian Survey on Disability, 2022
Scale: 27% of Canadians — approx. 8 million people — have a disability
  Youth (15–24): fastest-growing disability rate (2017–2022); most common: mental health & learning
  Working-age adults: mental health and pain-related disabilities most prevalent
  Seniors: pain-related, mobility, and flexibility challenges dominate
Key insight: disability is fluid and universal
  A broken arm, a baby stroller, aging eyes, or sensory overwhelm — everyone experiences disability at some point
  Disability types: mobility, vision, hearing, cognitive, neurological, pain-related, dexterity, memory

## Slide 12: Definitions
What is Barrier-free Access?
  Dictionary
      Design for those with physical or other disabilities, involving the provision of alternative means of access to steps (e.g. ramps and lifts (elevators) for those with mobility problems)
      National Building Code/Ontario Building Code
      Barrier-free means that a building and its facilities can be approached, entered, and used by persons with physical or sensory disabilities
      Canadian Standards Association (CSA B651)
      Accessible - as applied to a site, building, or other facility, possessing the necessary characteristics for it to be entered, exited, and used by people, including those with physical, sensory, or cognitive disabilities.

## Slide 13: Objectives
Barrier-free
  Remove barriers for people with disabilities, so that they may have access to and within a facility
  ADA
  Accessible Means of Egress. A continuous and unobstructed way of egress travel from any point in a building or facility that provides an accessible route to an area of refuge, a horizontal exit, or a public way.

## Slide 14: Objectives
Universal Design
  Universal design is defined as “the design of products and environments to be usable by all people, to the greatest extent possible, without the need for adaption or specialized design.”
  (Ronald Mace, 1988)

## Slide 15: Background
Barrier-free Accessibility vs. Universal Design
  Examples to Contrast “Barrier-free Accessibility” and “Universal Design”

## Slide 16: Background
Barrier-free Accessibility vs. Universal Design
  Examples to Contrast “Barrier-free Accessibility” and “Universal Design”
Typical devices that all people use

## Slide 17: Minimum (Code) Requirements

## Slide 18
Canadian Regulations
  Provinces in blue have accessibility acts
  There is a federal accessibility act, but it is for federally-owned buildings

## Slide 19
Canadian Regulations

## Slide 20
US Federal regulations

## Slide 21
Facility accessibility Design Standards (FADS)

## Slide 22
Codes Are Minimum
OBC/IASR set the legal minimum. Meeting code alone does not guarantee real usability or inclusive access for all users.
Snapshot in Time
Codes reflect the knowledge and political will at their drafting date. User needs, technology, and standards evolve faster than legislation.
Gaps in Scope
Building codes may not address libraries, cafeterias, specialized spaces, or outdoor environments comprehensively.
Enforcement Varies
Compliance is verified at time of permit — not continuously. Ongoing maintenance of accessible features is often inconsistent.
Conflict Between Standards
Code and other recognized accessibility design standards can conflict. Ambiguity exists on which governs; jurisdictional conflicts create compliance uncertainty.
Physical & Financial Constraints
Heritage buildings, structural limits, and budgets restrict what improvements are feasible even when desired.
Limitations of Current Accessibility Codes

## Slide 23
Human rights complaints • Reputational damage • Missed opportunities
⚖ Legal & Human Rights
AODA non-compliance can trigger complaints, audits, and fines. Human Rights Code obligations extend beyond building codes.
📉 Reputational Risk
Organizations perceived as inaccessible face community backlash, media scrutiny, and loss of public trust.
♿ User Exclusion
Technically compliant facilities can still be functionally unusable — defeating the purpose of accessibility for real users.
💰 Reactive Costs
Retrofitting discovered barriers post-construction is 3-5× more expensive than designing inclusively from the start.
📋 Regulatory Creep
Standards evolve. Today's compliant facility becomes tomorrow's deficient one without proactive planning.
🏛 Missed Revenue & Grant Eligibility
Government-funded capital programs require meeting or exceeding OBC accessibility levels as an eligibility criterion.
Risks of minimum only

## Slide 24: Emerging Trends in Accessibility
Image source: Accessibility Partners Canada
https://accessibilitypartners.ca/the-impact-of-accessibility-standards-on-construction/

## Slide 25
Recognize best practices and new standards
OBC
Ontario Building Code — Section 3.8
Baseline legislated standard. Barrier-free design for entrances, interior paths, and amenities (2024 Version).
IASR
Integrated Accessibility Standards Regulation
O. Reg. 191/11 under AODA. Addresses exterior paths of travel and accessible parking.
CSA B651
CSA B651-23 — Built Environment
2023 update reflects new powered wheelchair turning radii (2250mm), scooter dimensions (3150mm), and expanded guidance.
FADS
Facility Accessibility Design Standards
Municipal/organizational standards that exceed code (e.g. City of London FADS 2021). Wider doors, turning diameters, specialized facilities.
RHFAC
Rick Hansen Foundation Accessibility Certification
Independent third-party rating system assessing meaningful access. Goes beyond code.
Trends to Watch
→ Larger scooter & powered wheelchair dimensions in updated CSA B651-23
→ Growing adoption of organizational FADS exceeding code minimums
→ Neurodiversity & cognitive accessibility gaining recognition
→ "Accessibility by default" in procurement policies
→ Aging population driving demand (1 in 5 Canadians 65+ by 2030)
→ ADA benchmarking for Canadian organizations with US presence
Evolving Standards

## Slide 26
Evolving standards, demographics, and design approaches
👴 Aging Population Pressure
1 in 5 Canadians will be 65+ by 2030. Accessibility needs are shifting from minority to majority concern — driving policy reform and capital investment at scale.
🧠 Neurodiversity Recognition
Autism, ADHD, dyslexia, and cognitive differences are gaining formal recognition in design standards. CSA B651-23 now includes updated guidance on functional and cognitive barriers (Clause 4.7.1).
📐 Updated Dimensional Standards
CSA B651-23 reflects new anthropometric research: powered wheelchair turning radii increased to 2250mm, large scooters to 3150mm — many existing facilities built to older specs are now insufficient.
🏛 FADS Proliferation
More municipalities and institutions are developing Facility Accessibility Design Standards (FADS) that exceed minimum codes — signaling a broader cultural shift toward inclusive design as default.
🌍 Accessible Canada Act (ACA)
Accessibility Standards Canada is developing new national standards under the ACA, targeting a barrier-free Canada by 2040. Federal organizations face increasing compliance timelines and obligations.
♻ Accessibility + Sustainability Convergence
Universal design and green building goals are increasingly aligned. Accessible routes, adaptable spaces, and sensory-friendly environments also support energy efficiency and long-term flexibility.
Emerging trends

## Slide 27
From smart buildings to AI-powered navigation — what's coming and what it means for your facilities
AI & Smart Buildings
→ IoT sensors auto-adjust lighting, acoustics & door timing based on occupant needs in real-time
→ AI-driven systems learn individual user preferences and adapt environments proactively
→ Predictive maintenance flags failing accessible equipment (door operators, lifts) before they break
Indoor Navigation & Wayfinding
→ Smartphone apps using inertial sensors provide hands-free indoor navigation for blind users — no infrastructure needed (UC Santa Cruz, 2024)
→ GoodMaps uses LiDAR + computer vision to create 3D indoor maps with voice/haptic guidance
→ Evelity platform: inclusive wayfinding serving mobility, visual, hearing & cognitive users in complex venues
AR / VR & Digital Twins
→ AR glasses overlay real-time navigation directions on the user's field of view for visually impaired users
→ Digital Twins of buildings allow planners to simulate barrier removal before construction — reducing costly retrofits
→ VR used for stakeholder empathy training: experiencing a facility from a wheelchair user's or blind person's perspective
Neurodiversity & Cognitive Design
→ Sensory-inclusive design: quiet rooms, adjustable lighting zones, reduced visual clutter — emerging in schools & hospitals
→ Cognitive wayfinding: simplified pictogram signage, consistent spatial patterns, and predictable layouts
→ GPS-tracking wearables support independent navigation for users with cognitive impairments or dementia
Innovative Ideas

## Slide 28
Translating emerging developments into practical facility strategy
👁 Watch & Monitor
▸ Track CSA B651 updates — new anthropometric data may render existing compliant spaces insufficient
▸ Monitor Accessible Canada Act (ACA) standards pipeline — federal bodies are early adopters
▸ Follow FADS developments at peer organizations for benchmarking beyond minimum code
▸ Watch AI-assisted audit tools that may accelerate comprehensive assessments at lower cost
🧪 Pilot & Test
▸ Trial indoor wayfinding apps (GoodMaps, Evelity) at a high-traffic facility — measure user experience impact
▸ Introduce sensory rooms or quiet zones in one building as a neurodiversity pilot
▸ Deploy IoT-enabled accessible door operators with remote monitoring in a high-priority location
▸ Use digital twin or BIM models during capital projects to simulate barrier-free routes pre-construction
📌 Embed in Strategy
▸ Add 'technology-readiness' as a criterion in prioritization for capital planning — prioritize fixes that enable future accessibility upgrades
▸ Include accessibility technology in capital planning alongside physical barrier remediation
▸ Engage users with disabilities in pilot evaluations — lived experience validates technology effectiveness
▸ Build 'accessibility by default' into procurement policies: new equipment must meet current CSA standards
Organizational Strategy

## Slide 29: Choosing the assessment type
Types of Assessments to evaluate
your Facilities

## Slide 30: Back to KEY Questions
Are your facilities truly accessible, or just barely compliant?
How do I exceed minimum code requirements?
Selecting the most suitable audit and accessibility design standard
will help address these questions.

## Slide 31
Baseline Screening Checklist
High-level checklist
Barriers evaluated mainly based on observation (i.e. no measurements)
Ideal for:
  Quick evaluation of the building/site
  General understanding of accessibility in a large portfolio of assets
Evaluation is not definitive or conclusive
Baseline checklist can be customized based on needs

## Slide 32
Comprehensive Accessibility Audit
Detailed audit that compares the parameters of a barrier with OBC/IASR
Optional inclusion of FADS
Comprehensive audit evaluates compliance to the code or design guideline line-by-line
Ideal for:
  Confirmation of compliance to code/guideline
  Identifying specific areas requiring improvement

## Slide 33
Rick Hansen Survey
Similar to a comprehensive audit, but using the Rick Hansen Rating Survey / Scoring System
Ideal for:
  Promoting a particular asset (i.e. town hall)
  Comparing levels of meaningful access between various assets
Note: The Survey does not specifically address guidelines based on code

## Slide 34
Understanding Facility Needs
Baseline Screening
Checklist
With BCA
✓ High-level, time-efficient
✓ Identifies obvious barriers
✓ Delivered concurrently with BCA
✓ Good starting point for portfolios
Ideal for: High number of assets / quick triage
Comprehensive
Accessibility Audit
Detailed Understanding
✓ Line-by-line code comparison
✓ Captures all element types in scope
✓ Confirms compliance or identifies gaps
✓ Supports detailed recommendations
✓ Quantity-based remediation planning
Ideal for: Single facility focus / compliance confirmation
Rick Hansen Foundation Accessibility Certification (RHFAC) Survey
Third-Party Certification
✓ Independent certification
✓ Goes beyond code minimums
✓ Rates meaningful access
✓ Recognized publicly & by funders
Ideal for: Public-facing facilities / stakeholder communications
Auditing approach
✓ Identify specific barriers and locations

## Slide 35: Engaging Stakeholders in the Accessibility Journey

## Slide 36
Under the Ontario Human Rights Code, and Ontario Human Rights Act, owners/employers have a duty to accommodate persons with disabilities.
Under Title I of the ADA, there is a duty to provide reasonable accommodation in the workplace. Title III mandates there should be reasonable changes made for businesses.
Importance of Stakeholders
⚖ Legal & Human Rights
♿ Lived Experience
Understanding first-hand experience from users and occupants of your building, will help you identify barriers and possible solutions.
It will help target areas of priority and what the organization-specific needs are.

## Slide 37
Practical steps for meaningful participation
1
Identify
Stakeholders
Users, facility teams, disability orgs, finance, executive sponsors
2
Conduct
Consultation
On-site walkthroughs with users, focus groups, comment periods
3
Prioritize
Together
Apply Multi-Variable Prioritization (MVP) with stakeholder input on weights
4
Communicate
Progress
Transparency on barriers found, timelines, and remediation plans
5
Review &
Iterate
Annual reviews, updated audits, and continuous feedback loops
Key Principle: Accessibility planning is not a one-time event.
The most effective programs create feedback mechanisms that continuously capture user experience, incorporate new standards, and update the capital plan accordingly. Engaging those with lived experience of disability is not optional — it is essential to meaningful accessibility.
Engaging Stakeholders

## Slide 38: Limitations & Constraints

## Slide 39
Understand limitations that affect the ability to follow latest standards
Heritage Buildings
▸ Ontario Heritage Act allows modifications to defining features that would alter essential nature
▸ Assess heritage facilities individually for least-disruptive retrofit approach
▸ Equivalent facilitation proposals reviewed by Director on a case-by-case basis
▸ IASR provides documented exception pathways for cultural heritage properties
Financial & Budget Limits
▸ Prioritize high-occupancy, high-impact spaces first
▸ Integrate accessibility improvements into scheduled capital renewals
▸ Phased plans spread costs while demonstrating continuous progress
▸ Government-funded programs require meeting OBC accessibility as eligibility criterion
Physical & Structural
▸ Existing structural systems may limit door widths, turning radii, ramp grades
▸ Technical infeasibility must be documented — reduced dimensions are minimums, not targets
▸ Alterations that increase accessibility are always preferred even if full compliance is impossible
▸ No alteration should decrease existing accessibility below new-construction requirements
Real World Constraints &
How to Navigate Them

## Slide 40
One thing may be considered barrier-free (accessible) and not to another
Competing Standards
There could be things that are considered accessible or universally designed in some standards, but not in others.
For example:
There is a section for barrier-free design in CSA B44 for Destination Elevators.
However, in the RHFAC standard, it is mentioned:
Destination elevators, also known as destination dispatch, refer to elevators that use digital technology to assign passengers to specific elevator cabs that would take them to the floors they need to go, especially in high density buildings. While effective for managing large volumes of traffic, destination elevators very often barriers to accessibility for individual users with disabilities.
vs.

## Slide 41
One Improvement may be a Barrier to Another
Competing Improvements
Power door operators are helpful for all users, especially those that struggle with strength or dexterity.
However:
Power doors generally require more force to open manually
Doors may close on people who move slowly

## Slide 42
One Improvement may be a Barrier to Another
Competing Improvements
Conflict example | Affected user groups | Benefits | Downsides | Recommended compromise(s)
Tactile paving vs smooth surfaces | Helps: Blind and low vision (BLV); Hinders: mobility device users, older adults | Underfoot cues at hazards/decision points support independent mobility for BLV | Rough/textured surfaces can increase rolling resistance and vibration exposure for wheeled users | Keep primary paths smooth; confine tactile to hazards/decision points; provide bypass strip
Open-plan noisy spaces vs quiet rooms | Helps: supervision/collaboration; Hinders: DHH (deaf and hard hearing), neurodivergent, cognitive impairment | Visibility and informal communication | Noise harms satisfaction, productivity, and health outcomes in open-plan vs cellular offices | Acoustic zoning; quiet rooms; sound-absorptive finishes; “calm route” areas
Automatic doors with strong closing force vs manual handles | Helps: mobility/strength limits; Hinders: slower walkers, some cognitive/sensory users | Hands-free access; reduced force needed to open | Doors closing too quickly/forcefully can impede slower users; exterior force tradeoffs due to wind/pressure/seals | Low-energy operators where force high; tune closer speed; provide adequate maneuvering space
Bright uniform lighting vs low-stimulus lighting | Helps: low vision & safety; Hinders: neurodivergent, migraine, cognitive impairment | Uniform illumination reduces shadows and supports visibility | Brightness, flicker, glare, and color temperature can drive sensory discomfort; autistic participants report sensitivity to technical factors like brightness/flicker | Layered dimmable lighting; flicker control; “calm” zones; avoid high-gloss reflective finishes

## Slide 43
There is a lot of variety in lived experience
Subjectivity of lived experience
vs.
Consulting lived experience is key to accessibility improvements.
However, not all experiences of the same barrier may be the same.
Will need to understand:
Weigh various opinions
Importance of specific improvements to the organization
Consensus for accessibility improvements.

## Slide 44
“Bigger is not better”
The trend appears that particularly for mobility and access, size requirements continue to increase:
Wider turning diameters
Wider clear door widths
However, “bigger is not always better”.
Example: Tactile Attention Indicators
Designed with specific parameters (length, dome spacing, etc.)
Based on research and study
Suggest:
Refer to latest versions of accessibility design standards
Consult organization’s stakeholders

## Slide 45: Building a Future-Proof Accessibility Strategy
Image source: Holy Family Roman Catholic Separate School Division #140
https://www.holyfamilyrcssd.ca/index.php/announcements/holy-family-develops-accessibility-plan

## Slide 46
BUILDING A FUTURE-PROOF ACCESSIBILITY STRATEGY
Continuous improvement, risk management, and organizational strategy
🔍
ASSESS
Choose the right audit type for your organization. Baseline for portfolios; Comprehensive for detailed improvements or specific areas to address.
Choose the most suitable design guideline
→
📊
PRIORITIZE
Apply MVP framework. Weight factors by facility type, occupancy, deferral consequence, and standard level.
→
📋
PLAN
Integrate accessibility improvements into your capital plan. Phase investments across a multi-year horizon.
→
🤝
ENGAGE
Involve users, disability advocates, and leadership. Build accessibility into culture, not just construction.
In the construction design, seek feedback and implement latest trends.
→
🔄
MONITOR
Annual reviews. Track completed improvements. Update assessments when standards evolve or new needs emerge.

## Slide 47
KEY TAKEAWAYS
Compliance ≠ Accessibility
Meeting minimum code is the floor, not the ceiling. Real usability requires going further. Also, need to consider human rights.
Important: Meeting minimum code is necessary and legislated.
Know Your Standards
OBC, IASR, CSA B651, FADS, and RHFAC each serve different purposes. Use them strategically.
Choose the Right Audit
Baseline checklists triage; comprehensive audits confirm; RHFAC certifies. Match to your need.
Prioritize Strategically
Multi-Variable Prioritization integrates compliance, user impact, and capital planning into a defensible plan.
Plan for Constraints
Heritage, budget, and structural limits are real — but they are navigable with the right approach.
Future-Proof Continuously
Build a feedback loop: assess → prioritize → plan → engage → monitor → repeat.

## Slide 48: Q & A

## Slide 49: Thank you for attending
Connect with us directly!
  Andrew.Chow@rothiams.com
  accessibility@rothiams.com
  416-419-7143

## Slide 50: References & Sources
Standards & Legislation
  Ontario Building Code (OBC) Section 3.8, 2012 (2015 Amendment) | O. Reg. 191/11 IASR | AODA 2005 | ODA 2001
  Accessible Canada Act (ACA) 2019 | ADA Standards for Accessible Design, 2010 | Ontario Human Rights Code
Design Guidelines & Research
  CSA B651-23: Accessible Design for the Built Environment (CSA Group, January 2023)
  City of London Facility Accessibility Design Standards (FADS), 2021
  NC State University, Center for Universal Design — Principles of Universal Design, v2.0, 1997
  Tsai, C.H. et al. — Indoor Wayfinding Apps for Blind Travelers. ACM Trans. on Accessible Computing, 2024
  GoodMaps (goodmaps.com) | Evelity (evelity.com) | Statistics Canada — Canadian Survey on Disability, 2022
Roth IAMS Sources
  SOP 101 Accessibility On-Site Procedures (2026) | Accessibility Training (2025) | LAS Webinar Sept 2024